## Slide 1
Cache Mapping
CSCI 2400: Introduction to Computer Systems 18th Lecture, April 22nd , 2019
Spring 2019
Instructor: SANDESH DHAWASKAR SATHYANARAYANA
Email ID: sadh0344@Colorado.edu
Slides are adopted from CMU text book slides

## Slide 2: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
CPU looks first for data in cache
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory

## Slide 3: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 4: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 5: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 6: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes (= hit)
valid? +
block offset
tag

## Slide 7: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes (= hit)
valid? +
int (4 Bytes) is here
block offset
If tag doesn’t match (= miss): old line is evicted and replaced

## Slide 8: Direct-Mapped Cache Simulation
M=16 bytes (4-bit addresses), B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 9: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
2 lines per set
S sets

## Slide 10: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes (= hit)
block offset
tag

## Slide 11: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size B=8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes (= hit)
block offset
short int (2 Bytes) is here
No match (= miss):
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 12: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 13: What about writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Each cache line needs a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes straight to memory, does not load into cache)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate
0
1
2
B-1
tag
d
B = 2b bytes
dirty bit
v
valid bit

## Slide 14: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 15: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    4 clock cycle for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 16: Let’s think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider this simplified example: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 x 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 x 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 17: Lets solve some problems:
Practice Quiz 10
6.12,6.13,6.14 and 6.15
https://moodle.cs.colorado.edu/question/preview.php?id=1693420&cmid=37057&behaviour=deferredfeedback&maxmark=5.0000000&correctness=0&marks=1&markdp=2&feedback&generalfeedback&rightanswer&history
https://moodle.cs.colorado.edu/question/preview.php?id=1691416&cmid=37057&behaviour=deferredfeedback&maxmark=5.0000000&correctness=0&marks=1&markdp=2&feedback&generalfeedback&rightanswer&history